## Slide 1: Master Presentation

## Slide 2: Michael Quach

## Slide 3: Venus Exploration Propulsion System Design
Michael Quach
ARO 481lL-01
October 9th, 2023

## Slide 4: Introduction
Venus Orbiter Requirements
Mission ConOps
Orbiter Propulsion
Orbiter Mass Statement
Conclusion
Reference Slides
Courtesy:
Planetary Science Journal

## Slide 5: Mission Overview
Key Objectives
  Crewed mission of 4 orbiting around Venus to collect scientific data
  Launch no later than December 31, 2037
  Completion of mission no later than December 31, 2039
Assumptions
  Two-body problem (point-masses)
  Patched conics via Hohmann Transfers
  Problem is relative to the sun (Heliocentric reference frame)
  No considerations of perturbations
Parameters
  ( = 340 seconds
  ( = 400 seconds
  Various parking orbits
Courtesy:
Planetary Science Journal

## Slide 6: Landing Site and Scientific Goals
Landing Sites
  Alpha Regio: Largest highland regions on Venus near the Equator
  Beta Regio: Prominent highland with coronae structures
  Ishtar Terra: Highland region near the Northern Hemisphere – Maxwell Montes
  Aphrodite Terra: Highland region near the Southern Hemisphere
Scientific Goals
  Composition and structure of planet’s crust and mantle
  Analyzing the minerals and surface composition
  Analyzing and capturing the composition of the Venusian atmosphere
Courtesy:
DAVINCI

## Slide 7: System Level Requirements
Category | Description | Validation Method
T.0.0-1 | The orbiter must have the capacity for 4 crew members | Crew testing
T.0.0-2 | The orbiter shall have the ability to be controlled by the crew and collect samples | Hardware-in-the-loop
T.0.0-3 | The vehicle shall be parked in orbit such that it provides a desirable LOS and reliable data rate | In-flight mission
C.0.0-1 | Cost shall not exceed $1 Billion US dollars mission wide | System completion
M.0.0-1 | The mission shall be completed no later than December 31, 2039 lasting no longer than 30 Earth days | Mission completion
M.0.0-2 | Launch for the mission shall be no later than December 31, 2037 | Actual launch date

## Slide 8: Derived Requirements (1/2)
Category | SLR Reference | Description | Validation Method
T.1.1-1 | T.0.0-1 | The team shall make use of past NASA designs and utilize the average astronaut size to fit the whole crew with a extra space margin of ± 10% volume. | Crew testing
T.1.2-1 | T.0.0-2 | The team shall conduct latency tests with the orbiter on Earth mimicking the relay between the orbiter and crew spacecraft to verify a latency of < 0.1ms with a ±0.1%. | Hardware-in-the-loop testing
T.1.2-2 | T.0.0-2 | The orbiter shall have the capability of analyzing the Venusian atmosphere utilizing a suite of instruments. | Operation during mission
T.1.2-2.1 | T.1.2-2 | The laser spectrometer shall capture the key thermodynamic and surface composition properties within a ±.01% margin | Hardware-in-the-loop testing

## Slide 9: Derived Requirements (2/2)
Category | SLR Reference | Description | Validation Method
C.1.1-1 | C.0.0-1 | The team shall have regular meetings with the vendors to ensure that all projects are on-track. | Budget tracking
M.1.1-1 | M.0.0-1 | Trajectory team shall communicate with the logistics team to ensure the launch vehicle leaves within the optimal launch window. | Crew testing
M.1.2-1 | M.0.0-2 | Ground station shall keep in communication with the crew to ensure everything is operational within the module | Mission in operation

## Slide 10: Expected Venusian Atmospheric Properties
Altitude range (50-55 km)
  Density: 66.07 - 70 kg/m^3
  Temperature: 300-400 K
  Pressure: ~1-2 atm
  Zonal Wind Speed: 45-55 m/s
Courtesy: VIRA

## Slide 11: ConOps Diagram (Crew Module)
Total v: 17.74 km/s
Total Time: 302.74 days
(3) Crew module docks onto Gateway
(4) Crew module leaves Gateway to Venus
(5) Venus Orbit insertion
(6) Crew module establishes COMMs with the orbiter
Mission conducted
(7) Crew module leaves Venus
(8) Crew module attaches and leaves from Gateway
(2) Crew module detaches from SLS
(1) SLS enters parking orbit
(9) Crew module reenters into Earth

## Slide 12: ConOps Diagram (Spacecraft)
(5) Venus Orbit insertion
Total v: 6.38
Spacecraft v: 3.28
Total Time: 200 days
= 9.52
(6) Spacecraft enters Venusian atmosphere
(3) Spacecraft detaches from upper stage
(4) Mid-course correction
(2) Trans-Venus injection burn
(1) Upper stage and orbiter

## Slide 13: Mission In-depth (1/2)
(6) Crew module establishes COMMs with the orbiter
Mission conducted
(6.1) The orbiter will capture atmospheric data at various altitudes and deploy probes when commanded by the crew
(6.2) The orbiter will relay the data from itself and the probes back to the team
(6.3) Planned docking between the orbiter and crew to transfer over captured atmospheric capsules
(6.4) The orbiter will maintain its orbit until the mission duration and then descend into Venus’s orbit

## Slide 14: Mission In-depth (2/2)
(6.1)
Entry into Venus
(6.5)
Deploys main chute
(6.6)
Aeroshell separation
(6.7)
Probe enters free-fall
(6.2)
Back shell detaches
(6.3)
Deploys pilot chute
(6.4)
Extract chute bag
Average rate of descent: 0.1111 m/s

## Slide 15: Mission Operations
Altitude (km)
Time (Earth Hours)
45
50
55
60
0
120
Circumnavigation 1
Circumnavigation n
240
B
A
C
D
E
F
G
0
H

## Slide 16: Mission Operations Step-by-step (Balloon)
A.) After detaching from the aeroshell, the balloon will inflate
B.) The team will initialize the payload to begin collecting data
C.) The rest of the critical science instruments will be switched on by the crew
D.) The team will depressurize the balloon to lower the altitude via valve system
E.) The team will repressurized the balloon to keep it within the “goldilocks zone”
F.) The balloon will continue to depressurize the balloon when it reaches its max height
G.) The team will continue to repressurize the balloon when it reaches its lowest height
H.) Crew navigates the balloon to land on Alpha Regio

## Slide 17: Orbital Maneuvers Summary (Crew Module)
1.) Earth to Moon
  : 3.1609
  : 0.6104
  Transfer time: 4.917 days
2.) Moon to Venus
  : 1.8218
  3.2404
  Transfer time: 146.3964 days
3.) Venus to Moon
  : 3.3253
  : 1.8076
  Transfer time: 146.3964 days
4.) Earth to Moon
  : 0.6619
  : 3.1129
  Transfer time: 4.917 days

## Slide 18: Orbital Maneuvers Summary (Orbiter)
1.) Earth to Moon
  : 3.1609
  : 0.6104
  Transfer time: 4.917 days
2.) Moon to Venus
  : 1.8218
  3.2404
  Transfer time: 146.3964 days

## Slide 19: Launch Vehicle
SLS (Space Launch System) Block 2
  Core Stage (LH2 and LOX)
    Thrust: 2,280 kN
    : 452 seconds
  Solid Rocket Boosters (Aluminum and Ammonium Perchlorate)
    Thrust: 16,000 kN
    : 269 seconds
  Upper Stages (LH2 and LOX)
    Thrust: 930 kN
    : 465 seconds
Courtesy: NASA

## Slide 20: Propulsion System Analysis Assumptions
Assumptions
  = 330 MPa
  Ullage = 30%
  Total = 17.74
Titanium tanks
  = 690 MPa
  = 26.7 C
  = 4429.89
Courtesy:
NASA

## Slide 21: Orbiter Propulsion System Trade Study
Engine | Propellant Mass (kg) | Tank Volume () | Tank Mass (kg) | Wall Thickness (m)
SPT-140 Engine | 848.32 | 0.00265 | 8.266 | 0.000777
Aerojet Rocketdyne MR-106 Thrusters | 59,642 | .14629 | 2091.72 | 0.00575
Europa Clipper | 42,000 | 0.13 | 1406 | 0.00425
Engine | Propellant Mass (kg) |  | Tank Mass (kg) | Wall Thickness (m)
SPT-140 Engine | 848.32 | 0.00265 | 8.266 | 0.000777
Aerojet Rocketdyne MR-106 Thrusters | 59,642 | .14629 | 2091.72 | 0.00575
Europa Clipper | 42,000 | 0.13 | 1406 | 0.00425
Courtesy:
NASA

## Slide 22: Orbiter Propulsion System
SPT-140 Engine (Stationary Plasma Thruster )
  Isp = 1800 seconds
  Thrust: 280 mN
Propellant tank
  Propellant Mass: 848.32 kg of Xenon
  Volume = 0.00265
  Tank Mass = 8.2661 kg
  Tank radius: .002 meters
  Wall thickness: .00077 m
Courtesy: NASA

## Slide 23: Orbiter and Probe Instruments (1/2)
Tunable Laser Spectrometer (TLS)
  Analyze the composition of the Venusian atmosphere
Europa Clipper Magnetometer (ECM)
  Study Venus magnetic field and its interaction with solar wind
Mars Color Imager (MARCI)
  Different wavelength images of Venus, insights on cloud formations and dust storms
Courtesy:
NASA

## Slide 24: Orbiter and Probe Instruments (2/2)
MCS (Mars Climate Sounder)
  Analyzing cloud layers and composition
MASPEX (Mass Spectrometer for Planetary Exploration)
  Study composition of Venus atmosphere to determine planets geology and climate history
SEIS (Seismic Experiment for Interior Structure
  Gain insight on the interior of Venus through seismic vibrations
Courtesy: NASA

## Slide 25: Power Analysis Overview
Assumptions
  Source-to-loads transmission efficiency XSL : 0.95
  Array-to-battery transmission efficiency XAB : 0.70
  Battery-to-loads transmission efficiency XBL : 0.96
  Used planets’ gravitational parameter
  Circular orbits
Cases
  Low Earth Orbit (LEO): Altitude of 200 km
  Near Venus Surface: Altitude of 50 km

## Slide 26: Case 1 Analysis (LEO)
Inputs
  Altitude = 200 km
  Gravitational parameter, , = 398600
Outputs
  Time in daylight = 39.04 seconds
  Time in eclipse = 5270.61 seconds
  Minimum required power = 800.57 W
  *Power capacity in daylight = 5.77 Watt-hour

## Slide 27: Case 2 Analysis (Near Venus Surface)
Inputs
  Altitude = 50 km
  Gravitational parameter,, = 324859
Outputs
  Time in daylight =42.12 seconds
  Time in eclipse = 5212.50 seconds
  Minimum required power = 801.33 W
  *Power capacity in daylight = 9.17 Watt-hour

## Slide 28: Battery Sizing (Lithium)
  Energy supplied by battery, : 33019.53 J
  Total energy capacity, : 729 W-h
Specifications
  Required battery capacity: 24.55 A-h
  Nominal voltage: 29.7 V
  Number of cells per string: 4
  Number of cells per battery: 11
  Number of strings: 1
  Total battery mass: 10.8 kg
  Total battery energy capacity: 2376 W-h

## Slide 29: Solar Array Sizing
Surface area: 43.95
Solar array mass per area: 4.39 kg/m^2 (Magellan)
Solar array area: 12.6 m^2
Solar array mass: 55.314 kg
Not practical for mission due to Venusian atmosphere

## Slide 30: Alternate Power Source (Fuel Cells)
Power Source | Voltage (V) | Duration | Energy Capacity (WH) | Volume (m^3)
Fuel Cell | 28 | 1 month | 899201.52 | 0.55
Li/CFX | 28 | 10 years | 784 | 7.90 x 10^-4
MMRTG | 28 | 10 years | N/A | N/A

## Slide 31: Power System Block Diagram
Regulator
LOX Tank
LH2 Tank
Power Conditioning Unit (PCU)
Communication System
Fuel Cell
Payload
Thermal Control Unit
Gas Release System
Attitude Determination and Control System
Guidance Navigation and Control

## Slide 32: Orbiter Mass Statement (1/2)
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 117 | 105.931 | E
Structure | 260 | 260 | E
Thermal Control | 78 | 78 | E
Power | 195 | 195 | E
TT&C | 91 | 91 | E
On-Board Processing | 52 | 52 | E
ADC | 78 | 78 | E
Propulsion | 130 | 130 | E
Other (balance + launch) | 39 | 39 | E
Budget Total | 1040 | 1028.931 | 
Margin | 1976 | 1954.9689 | 

## Slide 33: Orbiter Mass Statement (2/2)
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 1976 | 1954.9689 | 
Propellant | 1430 | 848.3200363 | E
Pressurant | 6.3982061 | 3.795612889 | E
ON-ORBIT WET | 3406 | 2803.288936 | 
Adapter | 307.153 | 261.6483147 | C
Launch Mass | 3713.153 | 3064.937251 | E

## Slide 34: Spherical Assumptions
Wet Mass
Volume: 12.93
Radius: 1.456 m
Surface Area: 26.64
Area: 6.66
Dry Mass
Volume: 16.92
Radius: 1.59 m
Surface Area: 31.87
Area: 7.97 knl

## Slide 35: Conclusion
Trajectory
  = 8.87 km/s
  TOF = 151.3705 days
  =13.5609
Propulsion System
  SLS gets orbiter into LEO from Cape Canaveral
  The SPT-140, Hall-effect thrusters, provides the most efficient way to reach Venus
    = 1800 seconds
    Propellant Mass = 848.32 kg
  581.68 kg under the allocated propulsion budget
Notes: Design A
  Total time = 302.74 days
  Total DV = 17.74 km/s
Design B
  Total time = 292.14 days
  Total DV = 13.3141 km/s

## Slide 36: Reference Slide
[1] Brown, C. D. (2002). Elements of spacecraft design. American Institute of Aeronautics and Astronautics, Inc.
[2] Edberg, D. (2022). Spacecraft Design, Development, & Operation.
[3] Europa Clipper Instrument Summaries. (n.d.-a). https://europa.nasa.gov/internal_resources/379/ScienceInstruments_031422_Public.pdf
[4] Instructions for competitors obtaining own launch RevB - NASA. (n.d.-b). https://www.nasa.gov/wp-content/uploads/2023/02/instructions-for-competitors-obtaining-own-launch-revb.pdf
[5] NASA. (n.d.-a). Artemis. NASA. https://www.nasa.gov/specials/artemis/
[6] NASA. (2023, February 16). Maspex. NASA. https://europa.nasa.gov/spacecraft/instruments/maspex/
[7] NASA. (n.d.-b). NASA Technical Reports Server (NTRS). NASA. https://ntrs.nasa.gov/
[8] NASA. (n.d.-b). Radar Imager for mars’ subsurface exploration (RIMFAX). NASA. https://mars.nasa.gov/mars2020/spacecraft/instruments/rimfax/

## Slide 37: Reference Slide
[9] Space mission engineering: The new smad. (2011). . Amazon Publishing.
[10] Wikimedia Foundation. (2023, October 5). Xenon. Wikipedia. https://en.wikipedia.org/wiki/Xenon
[11] Wikimedia Foundation. (2023a, October 1). Psyche (spacecraft). Wikipedia. https://en.wikipedia.org/wiki/Psyche_(spacecraft)

## Slide 38: Thermal Design

## Slide 40: Orbiter Mass Statement (1/2)
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377.00 | 105.93 | C
Structure | 37000.00 | 35328.86 | C
Thermal Control | 1378.00 | 1015.00 | C
Power | 195.00 | 304.81 | C
TT&C | 91.00 | 91.00 | E
On-Board Processing | 52.00 | 52.00 | E
ADC | 78.00 | 78.00 | E
Propulsion | 130.00 | 4700.14 | C
Other (balance + launch) | 39.00 | 39.00 | E
TPS | 0.00 | 2516.99 | C
Budget Total | 39340.00 | 37014.61 | 
Margin | 13769.00 | 8877.27 | 

## Slide 41: Orbiter Mass Statement (2/2)
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 39340.00 | 37014.61 | 
Propellant | 100000.00 | 144078.67 | C
Pressurant | 447.43 | 644.65 | C
ON-ORBIT WET | 139340.00 | 181093.28 | 
Adapter | 10570.17 | 13722.54 | C
Launch Mass | 149910.17 | 202032.95 | C

## Slide 42: Orbiter Power Statement
Spacecraft Power Statement |  |  | 
Subsystem | Budget (W) | Current (W) | Status
Thermal Control | 170.369367 | 16.2496726 | C
Attitude Control | 121.692405 | 121.692405 | E
Power | 60.8462024 | 60.8462024 | C
CDS | 103.438544 | 103.438544 | E
COMMs | 139.946265 | 139.946265 | E
Propulsion | 6.08462024 | 6.08462024 | C
Mechanism | 6.08462024 | 6.08462024 | E
Total | 608.462024 | 454.34233 | E
Margin | 0 | 154.119694 | E
Payload | 170 | 144.2 | E
ON ORBIT POWER | 778.462024 | 598.54233 | 

## Slide 43: Thermal Analysis (Spherical Assumptions)
Wet Mass
  Volume: 12.93
  Radius: 1.456 m
  Surface Area: 26.64
  Area: 6.66
Dry Mass
  Volume: 16.92
  Radius: 1.59 m
  Surface Area: 31.87
  Area: 7.97

## Slide 44: Thermal Analysis
Inputs
  Maximum Power Dissipation: 144.2 W
  Minimum Power Dissipation: 80 W
  Altitude: 55 km
  Venus Radius: 6052 km
  IR Emissivity: 0.8
  Solar Absorptivity: 0.316
Outputs
  Worse case (Hot/Cold): 273 K / 208 K
  Radiator Area: 2.59 m^2
  Radiator Temperature (Worst Case Cold): 171 K
  Heater Power Required: 16.2 W
  Solar Array Temperature (Hot / Cold): 54.5 K / 41.5 K

## Slide 45: Conclusion
Thermal Analysis
  Worse case (Hot/Cold): 273 K / 208 K
  Radiator Area: 2.59 m^2
  Radiator Temperature (Worst Case Cold): 171 K
  Heater Power Required: 16.2 W
  Solar Array Temperature (Hot / Cold): 54.5 K / 41.5 K
Spacecraft Budgets
  Total Mass: 3833.79 kg (14.36% under budget)
  Total Power: 598.54 W (30.06% under budget)
  Values close to Perseverance Rover mission and Venus Express, but under Europa Clipper’s
Notes: Design A
  Total time = 302.74 days
  Total DV = 17.74 km/s
Design B
  Total time = 292.14 days
  Total DV = 13.3141 km/s

## Slide 46
Thank you!

## Slide 47: Power Design

## Slide 48: Power Analysis Overview
Assumptions
  Source-to-loads transmission efficiency XSL : 0.95
  Array-to-battery transmission efficiency XAB : 0.70
  Battery-to-loads transmission efficiency XBL : 0.96
  Used the planets’ gravitational parameter
  Circular orbits to simplify calculations
Cases
  Low Earth Orbit (LEO): Altitude of 200 km
  Near Venus Surface: Altitude of 50 km

## Slide 49: Case 1 Analysis (LEO)
Inputs
  Altitude = 200 km
  Gravitational parameter, , = 398600
Outputs
  Time in daylight: 39.04 seconds
  Time in eclipse: 5270.61 seconds
  Minimum required power: 800.57 W
  *Power capacity in daylight: 5.77 Watt-hour

## Slide 50: Case 2 Analysis (Near Venus Surface)
Inputs
  Altitude = 50 km
  Gravitational parameter,, = 324859
Outputs
  Time in daylight: 42.12 seconds
  Time in eclipse: 5212.50 seconds
  Minimum required power: 801.33 W
  *Power capacity in daylight: 6.28 Watt-hour

## Slide 51: Battery Sizing (Lithium)
  Energy supplied by battery, : 33019.53 J
  Total energy capacity, : 729 W-h
Specifications
  Required battery capacity: 24.55 A-h
  Nominal voltage: 29.7 V
  Number of cells per string: 4
  Number of cells per battery: 11
  Number of strings: 1
  Total battery mass: 10.8 kg
  Total battery energy capacity: 2376 W-h
Courtesy:
Eagle Picher

## Slide 52: Solar Array Sizing
  Surface area: 43.95
  Solar array mass per area: 4.39 (Magellan)
  Solar array area: 12.6
  Solar array mass: 55.314 kg
  Not practical for mission due to Venusian atmosphere
Courtesy:
NASA

## Slide 53: Alternate Power Source Trade Study
Power Source | Voltage (V) | Duration | Energy Capacity (WH) | Volume (m^3)
Fuel Cell | 28 | 1 month | 899201.52 | 0.55
Li/CFX | 28 | 10 years | 784 | 7.90 x 10^-4
MMRTG | 28 | 10 years | N/A | N/A

## Slide 54: Power System Block Diagram
Regulator
LOX Tank
LH2 Tank
Power Conditioning Unit (PCU)
Communication System
Fuel Cell
Payload
Thermal Control Unit
Gas Release System
Attitude Determination and Control System
Guidance Navigation and Control

## Slide 55: Orbiter Mass Statement (1/2)
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377 | 105.931 | C
Structure | 260 | 260 | E
Thermal Control | 1378 | 1015 | C
Power | 195 | 304.8140729 | C
TT&C | 91 | 91 | E
On-Board Processing | 52 | 52 | E
ADC | 78 | 78 | E
Propulsion | 130 | 37.6679819 | C
Other (balance + launch) | 39 | 39 | E
Cables | 0 | 143.8302505 | C
Budget Total | 2600 | 2155.15 | 
Margin | 0 | 484.85 | 

## Slide 56: Orbiter Mass Statement (2/2)
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 2600 | 2115.150743 | 
Propellant | 1430 | 1380.249811 | C
Pressurant | 6.3982061 | 6.175610324 | C
ON-ORBIT WET | 4030 | 3495.400554 | 
Adapter | 354.265 | 313.9027419 | C
Launch Mass | 4384.265 | 3809.303296 | E

## Slide 57: Orbiter Power Statement
Spacecraft Power Statement |  |  | 
Subsystem | Budget (W) | Current (W) | Status
Thermal Control | 170.369367 | 16.24967261 | C
Attitude Control | 121.692405 | 121.6924048 | E
Power | 60.8462024 | 6.283912758 | C
CDS | 103.438544 | 103.438544 | E
COMMs | 139.946265 | 139.9462655 | E
Propulsion | 6.08462024 | 2.42 | C
Mechanism | 6.08462024 | 6.084620238 | E
Total | 608.462024 | 396.1154199 | 
Margin | 0 | 212.3466039 | 
Payload | 170 | 144.2 | C
ON ORBIT POWER | 778.462024 | 540.3154199 | 

## Slide 58: Communication ConOps
Alpha Regio
S-band comms. Orbiter and crew module
X-band comms. crew module and Earth

## Slide 59: Science Instruments (2/2)
Atmospheric Structure Investigation Instrument
Measure atmospheric pressure & temperature during EDL
Descent Imager
Provide high quality imaging from under the clouds to the surface
Seismometer
Gain insight on the interior of Venus through seismic vibrations
Upper hazy sulfuric acid cloud layer
Thick concentrated sulfuric acid clouds
Clear layer of carbon dioxide
1985 Venus International Reference Atmosphere (VIRA)
Fine haze of sulfuric acid droplets & dust

## Slide 60: Probe Deployment and Science ConOps
Study high altitude atmospheric gases (50 – 40 km)
Analyze the layer most like Earths atmosphere (60 – 50 km)
Obtain knowledge of surface geology (20 km – surface)
Investigate the thick sulfuric cloud coverage (60 – 40 km)
Explore the atmosphere below the clouds (40 km – surface)
Altitude (km)
50
60
40
20
30
10
0
Utilize seismometer to study below the regolith (surface)
Measure clear layer of carbon dioxide (10 km – surface)

## Slide 61: Probe Orbit
0
120
Circumnavigation +n
240
Circumnavigation 1
Altitude (km)
50
60
Time (Earth Hours)
40
20
30
15
5
10
0

## Slide 62: Structural Design

## Slide 64: Mass and volume of Electronics
Subsystem | Mass (kg) | Volume ()
ACS | 78 | 0.24
Power | 304.81 | 0.27
C&DH | 52 | 0.16
Telecommunications | 91 | 0.28
Subsystem | Mass (kg) | 
ACS | 78 | 0.24
Power | 304.81 | 0.27
C&DH | 52 | 0.16
Telecommunications | 91 | 0.28

## Slide 65: Spacecraft First Look
  Volume: 14.03
  Surface area: 266.38
  Mass of launch vehicle adapter: 783.50 kg
  Total mass: 35328.86 kg

## Slide 66: Exploded-View and Call-outs
Cruise stage
Dinitrogen tank
Monomethyl hydrazine tank
Back shell
Heat shield
Fuel cell
Telecommunications
Helium tank
SEIS
TLS
MARCI
CD&H
MASPEX
Folded balloon
Payload structure

## Slide 67
4-View Drawing of Spacecraft

## Slide 68: Payload detached from aeroshell
  Volume: 3
  Surface area: 63.45

## Slide 69: Mass Properties and Stability
Spacecraft within Aeroshell
  Center of mass (meters):
    X = 0
    Y = 0.28
    Z = -0.29
  Moment of Inertia (kg-
    = 76222.31
    = 703926.38
    = 74078.52
    = 200.54
    = 63.69
    = 200.54
    =-2733.40
    = 63.69
    = -2733.40
Spacecraft without Aeroshell
  Center of mass (meters):
    X = -0.04
    Y = 0.69
    Z = -0.31
  Moment of Inertia (kg-
    = 4970.46
    = 4817.15
    = 4788.66
    = -68.52
    = 59.93
    = -68.52
    = -721.32
    = 59.93
    = -721.32

## Slide 70: Orbiter Mass Statement (1/2) - All
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377.00 | 105.93 | C
Structure | 37000.00 | 32734.63 | C
Thermal Control | 1378.00 | 1015.00 | C
Power | 195.00 | 304.81 | C
TT&C | 91.00 | 91.00 | E
On-Board Processing | 52.00 | 52.00 | E
ADC | 78.00 | 78.00 | E
Propulsion | 130.00 | 4380.12 | C
Other (balance + launch) | 39.00 | 39.00 | E
TPS | 0.00 | 2340.59 | C
Budget Total | 39340.00 | 34420.38 | 
Margin | 13769.00 | 105.93 | 

## Slide 71: Orbiter Mass Statement (2/2) - All
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 39340.00 | 34420.38 | 
Propellant | 100000.00 | 133980.68 | C
Pressurant | 447.43 | 599.47 | C
ON-ORBIT WET | 139340.00 | 168401.06 | 
Adapter | 10570.17 | 12764.28 | C
Launch Mass | 149910.17 | 187886.04 | C

## Slide 72: Orbiter Mass Statement (1/2) - SC
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377.00 | 105.93 | C
Structure | 260.00 | 2415.75 | C
Thermal Control | 1378.00 | 1015.00 | C
Power | 195.00 | 304.81 | C
TT&C | 91.00 | 91.00 | E
On-Board Processing | 52.00 | 52.00 | E
ADC | 78.00 | 78.00 | E
Propulsion | 130.00 | 570.16 | C
Other (balance + launch) | 39.00 | 39.00 | E
TPS | 0.00 | 2340.59 | C
Budget Total | 2600.00 | 4101.50 | 
Margin | 910.00 | -591.50 | 

## Slide 73: Orbiter Mass Statement (2/2) - SC
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 2600.00 | 4101.50 | 
Propellant | 1430.00 | 15964.99 | C
Pressurant | 6.40 | 71.43 | C
ON-ORBIT WET | 4030.00 | 20066.49 | 
Adapter | 354.27 | 1565.02 | C
Launch Mass | 4384.27 | 24542.26 | C

## Slide 74: List of Mechanisms
Mechanisms | Connection | Purpose
Cruise module detachment | Aeroshell | Detaches the cruise module from the system to reduce mass during entry
Aeroshell hatch | Aeroshell | Opens to allow the parachute to inflate and balloon soon after
Heat shield ejector | Back shell | Removes the heat shield to reduce mass during entry
Back shell ejector | Payload structure | Removes back shell to allow the balloon to expand outwards
Gas valve system | Payload structure | Inflates the balloon, which will be controlled by the team after
On-board thrusters/propellers | Payload structure | Controlled by the team to navigate the balloon to desired locations

## Slide 75: Conclusion
Spacecraft Overview
  Volume: 14.03
  Surface area: 266.38
  Mass of launch vehicle adapter: 783.50 kg
  Total mass: 35328.86 kg
Spacecraft Budgets
  Total Mass: 24542.26 kg (20.2% over budget)
    Within SLS’s payload mass capacity of 37,901 kg
Notes: Design A
  Total time = 302.74 days
  Total DV = 17.74 km/s
Design B
  Total time = 292.14 days
  Total DV = 13.3141 km/s

## Slide 76
With Aeroshell
Without Aeroshell

## Slide 77: Control System

## Slide 79: Exploded-View and Call-outs
Cruise stage
Dinitrogen tank
Monomethyl hydrazine tank
Back shell
Heat shield
Fuel cell
Telecommunications
Helium tank
SEIS
TLS
MARCI
CD&H
MASPEX
Folded balloon
Payload structure
ACS

## Slide 80: Exploded-View (ADC Specific)
Dinitrogen tank
Monomethyl hydrazine tank
Dinitrogen tank
Monomethyl hydrazine tank
4x Thrusters
4x Thrusters
ACS

## Slide 81: Top and Side View
5.0 meters
4.0 meters
1.0 meters
1.39 meters
1.07 meters
Z
Y
Top View
Side View

## Slide 82: Mass Properties and Stability
Spacecraft within Aeroshell
  Center of mass (meters):
    X = 0.01
    Y = 0.76
    Z = -0.30
  Moment of Inertia (kg-
    = 44451.50
    = 45161.45
    = 44017.00
    = 378.08
    = 108.92
    = 378.08
    = -3273.58
    = 108.92
    = -3273.58
Spacecraft without Aeroshell
  Center of mass (meters):
    X = -0.04
    Y = 0.69
    Z = -0.31
  Moment of Inertia (kg-
    = 4970.46
    = 4817.15
    = 4788.66
    = -68.52
    = 59.93
    = -68.52
    = -721.32
    = 59.93
    = -721.32

## Slide 83: ACS Engine Option 1
MOOG MONARC-1
1000+ used on space vehicles
Proven heritage in space applications

## Slide 84: ACS Engine Option 2
ECAPS 1N HPGP Thruster
102 currently in space
First flown on Prisma satellite (June 2010)

## Slide 85: ACS Engine Option 3
ArianeGroup 1N Monopropellant Thruster
500+ successful space operations
First flown on the Asterix 1 satellite in 1965

## Slide 86: ACS Engine Option 4
Aerojet Rocketdyne MR-103 1N
Flight proven 1000+ on space vehicles
First flown ATS 6 comsat (May 1974)

## Slide 87: ACS Engine Option 5
Aerojet Rocketdyne MR-111E 2N
Flight proven 500+ on space vehicles
First flown Intelsat 5 (December 1980)

## Slide 88: Attitude Control System Engine Options
 | MONARC-1 | 1N HPGP Thruster | 1N Monopropellant Thruster | MR-103D 1N | MR-111E 2N
Supplier | MOOG | ECAPS | ArianeGroup | Aerojet Rocketdyne | Aerojet Rocketdyne
Mass (kg) | 0.38 | 0.39 | 0.29 | 0.33 | 0.33
L x W (m) | 0.113 x 0.05 | 0.178 x 0.05* | 0.172 x 0.046 | 0.146 x 0.071 | 0.169 x 0.074
Power (W) | 18 | 12 | N/A | 13.7 | 13.6
Isp (sec) | 227.5 | 226.1 | 220 | 224 | 224
Propellant | Hydrazine | LMP-103S | Hydrazine | Hydrazine | Hydrazine
LMP-103S is a High-Performance Green Propellant (HPGP) offering up to a 30% better performance per volume than hydrazine according to the manufacturer ECAPS.
HPGP also contributes to Planet Protection Protocols.
*Estimated value
Engine
Characteristics

## Slide 89: Selected ACS Engine
Engine: 1N HPGP Thruster
Supplier: ECAPS
Mass: 0.39 kg
Dimensions: 0.172 x 0.05* m
ISP: 226.1 seconds
Propellant: LMP-103S

## Slide 90: Attitude Control System Thruster
  Mass: 0.38 kg
  Size: 0.178 m x .1m x .1m
  Isp: 231 seconds
  Supplier: ECAPS

## Slide 91: Aeroshell Time vs Euler Angles
Chart: Time vs Euler Angles
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300
Roll | 0 | 0.81278 | 3.2511 | 7.315 | 13.0044 | 20.3194 | 29.26 | 39.8261 | 52.0177 | 65.8349 | 81.2777 | 98.346 | 117.0399 | 137.3593 | 159.3043 | 182.8748 | 208.0709 | 234.8926 | 263.3398 | 293.4125 | 325.1108 | 358.4347 | 393.3841 | 429.9591 | 468.1596 | 507.9857 | 549.4373 | 592.5145 | 637.2172 | 683.5455 | 731.4994
Pitch | 0 | 0.8 | 3.2 | 7.2 | 12.8 | 20 | 28.8 | 39.2 | 51.2 | 64.8 | 80 | 96.8 | 115.2 | 135.2 | 156.8 | 180 | 204.8 | 231.2 | 259.2 | 288.8 | 320 | 352.8 | 387.2 | 423.2 | 460.8 | 500 | 540.8 | 583.2 | 627.2 | 672.8 | 720
Yaw | 0 | 0.8208 | 3.2832 | 7.3872 | 13.1328 | 20.52 | 29.5488 | 40.2192 | 52.5312 | 66.4848 | 82.08 | 99.3168 | 118.1952 | 138.7152 | 160.8768 | 184.68 | 210.1248 | 237.2112 | 265.9392 | 296.3089 | 328.3201 | 361.9729 | 397.2673 | 434.2033 | 472.7809 | 513.0001 | 554.8609 | 598.3633 | 643.5073 | 690.2929 | 738.7201

## Slide 92: Aeroshell Time vs Angular Velocity
Chart: Time vs Angular Velocity
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310
Roll Rate | 0.081278 | 0.24383 | 0.40639 | 0.56894 | 0.7315 | 0.89405 | 1.0566 | 1.2192 | 1.3817 | 1.5443 | 1.7068 | 1.8694 | 2.0319 | 2.1945 | 2.3571 | 2.5196 | 2.3571 | 2.1945 | 2.0319 | 1.8694 | 1.7068 | 1.5443 | 1.3817 | 1.2192 | 1.0566 | 0.89405 | 0.7315 | 0.56894 | 0.40639 | 0.24383 | 0.081278
Pitch Rate | 0.08 | 0.24 | 0.4 | 0.56 | 0.72 | 0.88 | 1.04 | 1.2 | 1.36 | 1.52 | 1.68 | 1.84 | 2 | 2.16 | 2.32 | 2.48 | 2.32 | 2.16 | 2 | 1.84 | 1.68 | 1.52 | 1.36 | 1.2 | 1.04 | 0.88 | 0.72 | 0.56 | 0.4 | 0.24 | 0.08
Yaw Rate | 0.08208 | 0.24624 | 0.4104 | 0.57456 | 0.73872 | 0.90288 | 1.067 | 1.2312 | 1.3954 | 1.5595 | 1.7237 | 1.8878 | 2.052 | 2.2162 | 2.3803 | 2.5445 | 2.3571 | 2.1945 | 2.0319 | 1.8694 | 1.7068 | 1.5443 | 1.3817 | 1.2192 | 1.0566 | 0.89405 | 0.7315 | 0.56894 | 0.40639 | 0.24383 | 0.081278

## Slide 93: Aeroshell Time vs Acceleration
Chart: Time vs Acceleration
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310
Roll Acceleration | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | 0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | 0.016256
Pitch Acceleration | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | 0.00026667
Yaw Acceleration | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | 0.016416 | -0.018743 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.016256 | -0.00054185

## Slide 94: Aeroshell Time vs Torque
Chart: Time vs Acceleration
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310
Torque (X) | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | 41400.9677
Torque (Y) | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677 | -41400.9677
Torque (Z) | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | 41400.9677 | -47268.8562 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857 | -40996.2857

## Slide 95: Aeroshell Time vs Propellant Mass
Chart: Time vs Propellant Mass Consumed
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310
Mass (X) | 0 | 0.039411 | 0.078822 | 0.11823 | 0.15764 | 0.19705 | 0.23646 | 0.27588 | 0.31529 | 0.3547 | 0.39411 | 0.43352 | 0.47293 | 0.51234 | 0.55175 | 0.59116 | 0.63057 | 0.66998 | 0.70939 | 0.74881 | 0.78822 | 0.82763 | 0.86704 | 0.90645 | 0.94586 | 0.98527 | 1.0247 | 1.0641 | 1.1035 | 1.1429 | 1.1823
Mass (Y) | 0 | 0.039411 | 0.078822 | 0.11823 | 0.15764 | 0.19705 | 0.23646 | 0.27588 | 0.31529 | 0.3547 | 0.39411 | 0.43352 | 0.47293 | 0.51234 | 0.55175 | 0.59116 | 0.63057 | 0.66998 | 0.70939 | 0.74881 | 0.78822 | 0.82763 | 0.86704 | 0.90645 | 0.94586 | 0.98527 | 1.0247 | 1.0641 | 1.1035 | 1.1429 | 1.1823
Mass (Z) | 0 | 0.039411 | 0.078822 | 0.11823 | 0.15764 | 0.19705 | 0.23646 | 0.27588 | 0.31529 | 0.3547 | 0.39411 | 0.43352 | 0.47293 | 0.51234 | 0.55175 | 0.59116 | 0.63057 | 0.66998 | 0.70939 | 0.74881 | 0.78822 | 0.82763 | 0.86704 | 0.90645 | 0.94586 | 0.98527 | 1.0247 | 1.0641 | 1.1035 | 1.1429 | 1.1823

## Slide 96: Spacecraft Time vs Euler Angles
Chart: Time vs Euler Angles
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300
Roll | 0 | 0.77532 | 3.1013 | 6.9779 | 12.4052 | 19.3831 | 27.9117 | 37.9909 | 49.6208 | 62.8013 | 77.5325 | 93.8143 | 111.6467 | 131.0299 | 151.9636 | 174.448 | 198.4831 | 224.0688 | 251.2052 | 279.8922 | 310.1298 | 341.9182 | 375.2571 | 410.1467 | 446.587 | 484.5779 | 524.1194 | 565.2116 | 607.8545 | 652.048 | 697.7922
Pitch | 0 | 0.8 | 3.2 | 7.2 | 12.8 | 20 | 28.8 | 39.2 | 51.2 | 64.8 | 80 | 96.8 | 115.2 | 135.2 | 156.8 | 180 | 204.8 | 231.2 | 259.2 | 288.8 | 320 | 352.8 | 387.2 | 423.2 | 460.8 | 500 | 540.8 | 583.2 | 627.2 | 672.8 | 720
Yaw | 0 | 0.80476 | 3.219 | 7.2428 | 12.8762 | 20.119 | 28.9713 | 39.4332 | 51.5046 | 65.1855 | 80.476 | 97.3759 | 115.8854 | 136.0044 | 157.7329 | 181.0709 | 206.0185 | 232.5755 | 260.7421 | 290.5182 | 321.9038 | 354.899 | 389.5036 | 425.7178 | 463.5415 | 502.9747 | 544.0175 | 586.6697 | 630.9315 | 676.8028 | 724.2836

## Slide 97: Aeroshell Time vs Angular Velocity
Chart: Time vs Angular Velocity
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310
Roll Rate | 0.077532 | 0.2326 | 0.38766 | 0.54273 | 0.69779 | 0.85286 | 1.0079 | 1.163 | 1.3181 | 1.4731 | 1.6282 | 1.7832 | 1.9383 | 2.0934 | 2.2484 | 2.4035 | 2.2484 | 2.0934 | 1.9383 | 1.7832 | 1.6282 | 1.4731 | 1.3181 | 1.163 | 1.0079 | 0.85286 | 0.69779 | 0.54273 | 0.38766 | 0.2326 | 0.077532
Pitch Rate | 0.08 | 0.24 | 0.4 | 0.56 | 0.72 | 0.88 | 1.04 | 1.2 | 1.36 | 1.52 | 1.68 | 1.84 | 2 | 2.16 | 2.32 | 2.48 | 2.32 | 2.16 | 2 | 1.84 | 1.68 | 1.52 | 1.36 | 1.2 | 1.04 | 0.88 | 0.72 | 0.56 | 0.4 | 0.24 | 0.08
Yaw Rate | 0.080476 | 0.24143 | 0.40238 | 0.56333 | 0.72428 | 0.88524 | 1.0462 | 1.2071 | 1.3681 | 1.529 | 1.69 | 1.8509 | 2.0119 | 2.1729 | 2.3338 | 2.4948 | 2.2484 | 2.0934 | 1.9383 | 1.7832 | 1.6282 | 1.4731 | 1.3181 | 1.163 | 1.0079 | 0.85286 | 0.69779 | 0.54273 | 0.38766 | 0.2326 | 0.077532

## Slide 98: Aeroshell Time vs Acceleration
Chart: Time vs Acceleration
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310
Roll Acceleration | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | 0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | 0.015506
Pitch Acceleration | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | -0.016 | 0.00026667
Yaw Acceleration | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | 0.016095 | -0.024631 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.015506 | -0.00051688

## Slide 99: Spacecraft Time vs Torque
Chart: Time vs Torque
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310
Torque (X) | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | 4416.0378
Torque (Y) | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378 | -4416.0378
Torque (Z) | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | 4416.0378 | -6758.0982 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164 | -4254.5164

## Slide 100: Aeroshell Time vs Propellant Mass
Chart: Time vs Propellant Mass Consumed
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310
Mass (X) | 0 | 0.0042038 | 0.0084075 | 0.012611 | 0.016815 | 0.021019 | 0.025223 | 0.029426 | 0.03363 | 0.037834 | 0.042038 | 0.046241 | 0.050445 | 0.054649 | 0.058853 | 0.063056 | 0.06726 | 0.071464 | 0.075668 | 0.079871 | 0.084075 | 0.088279 | 0.092483 | 0.096686 | 0.10089 | 0.10509 | 0.1093 | 0.1135 | 0.11771 | 0.12191 | 0.12611
Mass (Y) | 0 | 0.0042038 | 0.0084075 | 0.012611 | 0.016815 | 0.021019 | 0.025223 | 0.029426 | 0.03363 | 0.037834 | 0.042038 | 0.046241 | 0.050445 | 0.054649 | 0.058853 | 0.063056 | 0.06726 | 0.071464 | 0.075668 | 0.079871 | 0.084075 | 0.088279 | 0.092483 | 0.096686 | 0.10089 | 0.10509 | 0.1093 | 0.1135 | 0.11771 | 0.12191 | 0.12611
Mass (Z) | 0 | 0.0042038 | 0.0084075 | 0.012611 | 0.016815 | 0.021019 | 0.025223 | 0.029426 | 0.03363 | 0.037834 | 0.042038 | 0.046241 | 0.050445 | 0.054649 | 0.058853 | 0.063056 | 0.06726 | 0.071464 | 0.075668 | 0.079871 | 0.084075 | 0.088279 | 0.092483 | 0.096686 | 0.10089 | 0.10509 | 0.1093 | 0.1135 | 0.11771 | 0.12191 | 0.12611

## Slide 101: Worst Case Scenario (Aeroshell)
Assumptions:
  Magnetic field is negligible on Venus
  = 19.63
= [1.66, 1.66, 1.66] x N-m
= [21.56, 20.89, 21.99] N-m
= [-21.20, -20.21, -21.83] N-m
= [0, 0, 0] N-m

## Slide 102: Worst Case Scenario (Spacecraft)
Assumptions:
  Magnetic field is negligible on Venus
  = 7
= [5.96, 1.66, 1.66] x N-m
= [7.06, 7.52, 7.61] N-m
= [-0.457, -0.50, -0.51] N-m
= [0, 0, 0] N-m

## Slide 103: Reaction Wheel Unloading (Aeroshell)
Assumptions
  Momentum capacity: 12 N-m-s
  Torque: 0.2 N-m
  Spin-up time: 60 seconds
  Spin-down time: 60 seconds
Outputs
  Total time to unload: 3.81 seconds
  Propellant needed: .0015 kg
Courtesy:
Honeywell

## Slide 104: Reaction Wheel Unloading (Spacecraft)
Assumptions
  Momentum capacity: 12 N-m-s
  Torque: 0.2 N-m
  Spin-up time: 60 seconds
  Spin-down time: 60 seconds
Outputs
  Total time to unload: 35.68 seconds
  Propellant needed: .001 kg
Courtesy:
Honeywell

## Slide 105: Propulsion System Schematic (Aeroshell)

## Slide 106: ACS Block Diagram (Aeroshell)
Memory
Power *PCI Bridge
RAD750 CPU
Sun Sensors
2 x Computer
Star Tracker
Magnetometer
Central Moment Gyroscopes
Reaction Wheels
Thrusters
* Peripheral Component Interconnect

## Slide 107: Propulsion System Schematic (Spacecraft)
  For the moment, the aeroshell and spacecraft shall the same propulsion set-up until a more in-depth review

## Slide 108: ACS Block Diagram (Spacecraft)
Memory
Power *PCI Bridge
RAD750 CPU
Sun Sensors
2 x Computer
Magnetometer
Central Moment Gyroscopes
Reaction Wheels
* Peripheral Component Interconnect

## Slide 109: Aeroshell ADC Components
Aeroshell |  |  |  |  |  | 
Component | Quantity | Mass (kg) | Power (W) | Supplier | Total Line Mass (kg) | Total Line Power (W)
Star Tracker | 1 | 0.042 | 0.685 | AAC Clyde Space | 0.042 | 0.685
Sun Sensors | 1 | 0.029 | 5 | AAC Clyde Space | 0.029 | 5
Magnetometers | 1 | 0.1 | 1.02 | AAC Clyde Space | 0.1 | 1.02
RWAs | 1 | 9.5 | 22 | Honeywell | 9.5 | 22
CMGs | 1 | 1.9 | 12 | GranStal Solutions | 1.9 | 12
Computers | 1 | 0.549 | 35 | BAE Systems | 0.549 | 35
Thrusters | 4 | 0.38 | 10 | ECAPs | 1.52 | 40
 |  |  |  | Total | 13.64 | 115.705

## Slide 110: Spacecraft ADC Components
Spacecraft |  |  |  |  |  | 
Component | Quantity | Mass (kg) | Power (W) | Supplier | Total Line Mass (kg) | Total Line Power (W)
Magnetometers | 1 | 0.1 | 1.02 | AAC Clyde Space | 0.1 | 1.02
CMGs | 1 | 1.9 | 12 | GranStal Solutions | 1.9 | 12
Computers | 1 | 0.549 | 35 | BAE Systems | 0.549 | 35
 |  |  |  | Total | 2.549 | 48.02

## Slide 111: Orbiter Mass Statement (1/2) - All
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377.00 | 105.93 | C
Structure | 37000.00 | 14482.92 | C
Thermal Control | 1378.00 | 1015.00 | C
Power | 195.00 | 304.81 | C
TT&C | 91.00 | 91.00 | E
On-Board Processing | 52.00 | 52.00 | E
ADC | 78.00 | 35.28 | C
Propulsion | 130.00 | 2104.97 | C
Other (balance + launch) | 39.00 | 39.00 | E
TPS | 0.00 | 1096.56 | C
Budget Total | 39340.00 | 16125.94 | 
Margin | 13769.00 | 33781.53 | 

## Slide 112: Orbiter Mass Statement (2/2) - All
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 39340.00 | 16125.94 | 
Propellant | 100000.00 | 62769.93 | C
Pressurant | 447.43 | 280.85 | C
ON-ORBIT WET | 139340.00 | 78895.87 | 
Adapter | 10570.17 | 6006.64 | C
Launch Mass | 149910.17 | 88104.04 | C

## Slide 113: Orbiter Mass Statement (1/2) - SC
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377.00 | 105.93 | C
Structure | 260.00 | 3423.33 | C
Thermal Control | 1378.00 | 1015.00 | C
Power | 195.00 | 304.81 | C
TT&C | 91.00 | 91.00 | E
On-Board Processing | 52.00 | 52.00 | E
ADC | 78.00 | 5.10 | C
Propulsion | 130.00 | 148.76 | C
Other (balance + launch) | 39.00 | 39.00 | E
TPS | 0.00 | 1096.56 | C
Budget Total | 2600.00 | 5036.17 | 
Margin | 910.00 | -1526.17 | 

## Slide 114: Orbiter Mass Statement (2/2) - SC
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 2600.00 | 5036.17 | 
Propellant | 1430.00 | 3778.50 | C
Pressurant | 6.40 | 16.91 | C
ON-ORBIT WET | 4030.00 | 8814.67 | 
Adapter | 354.27 | 715.51 | C
Launch Mass | 4384.27 | 10775.50 | C

## Slide 115: Total System Power Statement
Spacecraft Power Statement |  |  | 
Subsystem | Budget (W) | Current (W) | Status
Thermal Control | 175.708471 | 17.2075243 | C
Attitude Control | 125.50605 | 328.43 | C
Power | 62.7530252 | 373.229155 | C
CDS | 106.680143 | 106.680143 | E
COMMs | 144.331958 | 144.331958 | E
Propulsion | 6.27530252 | 2.42 | C
Mechanism | 6.27530252 | 6.27530252 | E
Total | 627.530252 | 978.574082 | 
Margin | 564.777227 | 213.733397 | 
Payload | 170 | 152.7 | C
ON ORBIT POWER | 797.530252 | 1131.27408 | 

## Slide 116: Conclusion
Spacecraft Overview
  Number of thrusters: 8 in total (4 for aeroshell and 4 for spacecraft)
  Atmospheric and gravity gradient perturbations are the most significant
  ~150 seconds for each rotation to reach 180 degrees
Spacecraft Budgets
  Total spacecraft mass: 10775.50 kg (60% over budget)
    Within SLS’s payload mass capacity of 37,901 kg
  Total spacecraft power: 1131.27W (30% over budget)
Notes: Design A
  Total time = 302.74 days
  Total DV = 17.74 km/s
Design B
  Total time = 292.14 days
  Total DV = 13.3141 km/s

## Slide 117: Communications

## Slide 119: High-Gain Downlink Assumptions
  DSN 34-meter HES station (T9.15)
  Pointing accuracy: 0.1°
  Transmitter power: 25W
  Frequency: 8.42 GHz
  Cable loss (transmitter to antenna): 0.62dB
  Modulation index: 68°
  2.5 meter parabolic dish
  Polarization loss: 0.20 dB
  Receiver cable loss: 0.0 dB
  BER: 0.001

## Slide 120: High-Gain Downlink Analysis
Maximum range (1.53 km):
  Carrier SNR achieved: 37.31 dB
  Carrier link margin: 27.31 dB
  Data symbol rate: -52.53 dB-Hz
  SNR achieved: 12.66 dB
  Data link margin: 8.16 dB
Minimum range (1.46 km):
  Carrier SNR achieved: 37.73 dB
  Carrier link margin: 27.73 dB
  Data symbol rate: -52.53 dB-Hz
  SNR achieved: 13.07 dB
  Data link margin: 8.57 dB
  To achieve a data link margin greater than 10dB, a symbol rate of 125 sps would be required

## Slide 121: High-Gain Emergency Uplink Assumptions
  DSN 34-meter HES station (T9.15)
  Pointing loss: 0.1 dB
  Transmitter power: 30W
  Frequency: 8.42 GHz
  Cable loss (transmitter to antenna): 0 dB
  Modulation index: 57.30°
  2.5 meter parabolic dish
  Polarization loss: 0.20 dB
  Receiver cable loss: 0.0 dB
  BER: 1 x
  Symbol rate: 100 sps

## Slide 122: High-Gain Uplink Analysis
  Carrier SNR achieved: 37.93 dB
  Carrier link margin: 27.93 dB
  Data symbol rate: -50.00 dB-Hz
  SNR achieved: 14.96 dB
  Data link margin: 10.46 dB

## Slide 123: C&DS and Telecommunications Block Diagram (Aeroshell and Spacecraft)
Memory
Power *PCI Bridge
RAD750 CPU
Storage
2 x Computer
Power System
Thermal System
Payload
ADCS
Communication Subsystem
* Peripheral Component Interconnect

## Slide 124: Aeroshell Telecommunications Components
Aeroshell |  |  |  |  |  | 
Component | Quantity | Mass (kg) | Power (W) | Supplier | Total Line Mass (kg) | Total Line Power (W)
Computers | 2 | 0.55 | 35 | BAE Systems | 1.098 | 70
X-Band Transceiver | 1 | 0.2 | 16 | Spacecom | 0.2 | 16
X-Band Transponder | 1 | 3.2 | 15.8 | General Dynamics | 3.2 | 15.8
X-Band Antenna | 1 | 0.25 | 26 | CubeCom | 0.25 | 26
X-band Diplexer | 1 | 0.120 | 0 | CubeCom | 0.120 | 0
X-Band Splitter | 1 | 0.03 | 0 | CubeCom | 0.03 | 0
X-band Coupler | 1 | 0.035 | 0 | CubeCom | 0.035 | 0
X-Band Power Amplifier | 2 | 1.37 | 65.5 | General Dynamics | 2.74 | 131
 |  |  |  | Total | 7.67 | 258.8

## Slide 125: Aeroshell C&DS Components
Aeroshell |  |  |  |  |  | 
Component | Quantity | Mass (kg) | Power (W) | Supplier | Total Line Mass (kg) | Total Line Power (W)
Computers | 2 | 0.549 | 35 | BAE Systems | 1.098 | 70
Storage | 3 | 0.75 | 5 | Mercury | 2.25 | 15
FPGA | 2 | 0.28 | 3 | STM | 0.56 | 6
 |  |  |  | Total | 3.908 | 91

## Slide 126: Spacecraft Telecommunications Components
Spacecraft |  |  |  |  |  | 
Component | Quantity | Mass (kg) | Power (W) | Supplier | Total Line Mass (kg) | Total Line Power (W)
Computers | 2 | 0.549 | 35 | BAE Systems | 1.10 | 70
S-Band Transceiver | 1 | 0.2 | 15 | Spacecom | 0.2 | 15
S-Band Transponder | 1 | 2.722 | 46 | General Dynamics | 2.722 | 46
S-Band Antenna | 1 | 0.137 | 12 | CubeCom | 0.137 | 12
S-Band Diplexer | 1 | 0.22 | 0 | CubeCom | 0.22 | 0
S-Band Splitter | 1 | 0.02 | 0 | CubeCom | 0.02 | 0
S-Band Coupler | 1 | 0.032 | 0 | CubeCom | 0.032 | 0
S-Band Amplifier | 2 | 1.98 | 8.3 | General Dynamics | 3.96 | 16.6
 |  |  |  | Total | 8.389 | 159.6

## Slide 127: Spacecraft C&DS Components
Aeroshell |  |  |  |  |  | 
Component | Quantity | Mass (kg) | Power (W) | Supplier | Total Line Mass (kg) | Total Line Power (W)
Computers | 2 | 0.549 | 35 | BAE Systems | 1.098 | 70
Storage | 3 | 0.75 | 5 | Mercury | 2.25 | 15
FPGA | 2 | 0.28 | 3 | STM | 0.56 | 6
 |  |  |  | Total | 3.908 | 91

## Slide 128: Orbiter Mass Statement (1/2) - All
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377.00 | 77.43 | C
Structure | 37000.00 | 4423.00 | C
Thermal Control | 1378.00 | 1015.00 | C
Power | 195.00 | 304.81 | C
TT&C | 91.00 | 16.06 | C
On-Board Processing | 52.00 | 7.82 | C
ADC | 78.00 | 35.28 | C
Propulsion | 130.00 | 804.66 | C
Other (balance + launch) | 39.00 | 21.00 | C
Cables | 0.00 | 401.23 | C
Budget Total | 39340.00 | 5900.39 | 
Margin | 13769.00 | 46002.72 | 

## Slide 129: Orbiter Mass Statement (2/2) - All
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 39340.00 | 5900.39 | 
Propellant | 100000.00 | 22967.18 | C
Pressurant | 447.43 | 102.76 | C
ON-ORBIT WET | 139340.00 | 28867.57 | 
Adapter | 10570.17 | 2229.50 | C
Launch Mass | 149910.17 | 32302.95 | C

## Slide 130: Orbiter Mass Statement (1/2) - SC
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377.00 | 77.43 | C
Structure | 260.00 | 3423.33 | C
Thermal Control | 1378.00 | 1015.00 | C
Power | 195.00 | 304.81 | C
TT&C | 91.00 | 8.39 | C
On-Board Processing | 52.00 | 3.91 | C
ADC | 78.00 | 5.10 | C
Propulsion | 130.00 | 143.65 | C
Other (balance + launch) | 39.00 | 10.00 | C
TPS | 0.00 | 401.23 | C
Budget Total | 2600.00 | 4847.97 | 
Margin | 910.00 | -1337.97 | 

## Slide 131: Orbiter Mass Statement (2/2) - SC
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 2600.00 | 4847.97 | 
Propellant | 1430.00 | 3637.29 | C
Pressurant | 6.40 | 16.27 | C
ON-ORBIT WET | 4030.00 | 8485.26 | 
Adapter | 354.27 | 690.64 | C
Launch Mass | 4384.27 | 9720.78 | C

## Slide 132: Total System Power Statement
Spacecraft Power Statement |  |  | 
Subsystem | Budget (W) | Current (W) | Status
Thermal Control | 157.421476 | 14.1423988 | C
Attitude Control | 112.443911 | 328.43 | C
Power | 56.2219556 | 328.97595 | C
C&DS | 95.5773246 | 182 | C
COMMs | 129.310498 | 418.4 | C
Propulsion | 5.62219556 | 2.42 | C
Mechanism | 5.62219556 | 4.5 | C
Total | 562.219556 | 1278.86835 | 
Margin | 505.997601 | -210.651192 | 
Payload | 170 | 125.5 | C
ON ORBIT POWER | 732.219556 | 1404.36835 | 

## Slide 133: Conclusion
Telecommunication and C&DS (within compliance)
  X-band: Aeroshell to communicate back to ground station
  S-band: Spacecraft to communicate with the crew module
  Expected data link margin: 8.16 dB | 8.57 dB
  Expected data link margin (Emergency): 10.46 dB
Spacecraft Budgets
  Total spacecraft mass: 32302.95 kg (14.54% over budget)
    Within SLS’s payload mass capacity of 37,901 kg
  Total spacecraft power: 1404.37W (47.86% over budget)
Notes: Design A
  Total time = 302.74 days
  Total DV = 17.74 km/s
Design B
  Total time = 292.14 days
  Total DV = 13.3141 km/s

## Slide 134: Cost (Hw #12)

## Slide 136: Venus Exploration Cost Estimation
Michael Quach
ARO 481lL-02
November 20th, 2023

## Slide 137: Introduction
Overview and Requirements
Mission ConOps
Communication Analysis
Mass and Power Statements
Conclusion
References

## Slide 138: Mission Overview
Key Objectives
  Crewed mission of 4 orbiting around Venus to collect scientific data
  Launch no later than December 31, 2037
  Completion of mission no later than December 31, 2039
  What added science can be achieved with crew around Venus?
Scientific Goals
  Composition and structure of planet’s crust and mantle
  Analyzing the minerals and surface composition
  Analyzing and capturing the composition of the Venusian atmosphere
Courtesy:
DAVINCI

## Slide 139: Porkchop Plots
Departure Date (Updated): July 1st, 2035
Arrival Date (Updated): January 17th, 2036
Transfer Time: 200 [days]
Departure C3: 9.53 [km^2/s^2]
Arrival : 2.50 [km/s]
Capture DV: 3.29 km/s (Calculated)
Useful Spacecraft Mass: 37,900 [kg] (edited)

## Slide 140: ConOps Diagram (Crew Module)
Total v: 17.74 km/s
Total Time: 302.74 days
(3) Crew module docks onto Gateway
(4) Crew module leaves Gateway to Venus
(5) Venus Orbit insertion
(6) Crew module establishes COMMs with the orbiter
Mission conducted
(7) Crew module leaves Venus
(8) Crew module attaches and leaves from Gateway
(2) Crew module detaches from SLS
(1) SLS enters parking orbit
(9) Crew module reenters into Earth

## Slide 141: ConOps Diagram (Spacecraft)
(5) *Venus Orbit insertion
Total v: 6.38
Spacecraft v: 3.29
Total Time: 200 days
= 9.52
(6) *Spacecraft enters Venusian atmosphere
(3) Spacecraft detaches from upper stage
(4) *Mid-course correction
(2) Trans-Venus injection burn
(1) Upper stage and orbiter
*Affects design of attitude control system

## Slide 142: Mission In-depth (2/2)
(6.1)
Entry into Venus
(6.5)
Deploys main chute
(6.6)
Aeroshell separation
(6.7)
Probe enters free-fall
(6.2)
Back shell detaches
(6.3)
Deploys pilot chute
(6.4)
Extract chute bag
Average rate of descent: 0.1111 m/s

## Slide 143: Mission Operations
Altitude (km)
Time (Earth Hours)
45
50
55
60
0
120
Circumnavigation 1
Circumnavigation n
240
B
A
C
D
E
F
G
0
H

## Slide 144: Mission Operations Step-by-step (Balloon)
A.) After detaching from the aeroshell, the balloon will inflate
B.) The team will initialize the payload to begin collecting data
C.) The rest of the critical science instruments will be switched on by the crew
D.) The team will depressurize the balloon to lower the altitude through a valve system
E.) The team will repressurized the balloon to keep it within the “goldilocks zone”
F.) The balloon will continue to depressurize the balloon when it reaches its max height
G.) The team will continue to repressurize the balloon when it reaches its lowest height
H.) Crew navigates the balloon to land on Alpha Regio near its end of life

## Slide 145: Expected Venusian Atmospheric Properties
Altitude range (50-55 km)
  Density: 66.07 - 70 kg/m^3
  Temperature: 300-400 K
  Pressure: ~1-2 atm
  Zonal Wind Speed: 45-55 m/s
Courtesy: VIRA

## Slide 146: Stowed 2-View
19.1 meters
8.4 meters
7.5 meters
1.7 m
1.75 meters
Z
Y

## Slide 147: Side and Top View
1.39 meters
1.07 meters
Side View
5.0 meters
4.0 meters
1.0 meters
Top View
Z
Y

## Slide 148: Exploded-View and Call-outs
Cruise stage
Dinitrogen tank
Monomethyl hydrazine tank
Back shell
Heat shield
Fuel cell
Telecommunications
Helium tank
SEIS
TLS
MARCI
C&DS
MASPEX
Folded balloon
Payload structure
ACS

## Slide 149: Orbiter Mass Statement (1/2) - All
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377.00 | 77.43 | C
Structure | 37000.00 | 3923.00 | C
Thermal Control | 1378.00 | 1015.00 | C
Power | 195.00 | 304.81 | C
TT&C | 91.00 | 16.06 | C
On-Board Processing | 52.00 | 7.82 | C
ADC | 78.00 | 35.28 | C
Propulsion | 130.00 | 739.78 | C
Other (balance + launch) | 39.00 | 21.00 | C
Cables | 0.00 | 367.23 | C
Budget Total | 39340.00 | 5400.39 | 
Margin | 13769.00 | 46601.59 | 

## Slide 150: Orbiter Mass Statement (2/2) - All
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 39340.00 | 5400.39 | 
Propellant | 100000.00 | 21020.94 | C
Pressurant | 447.43 | 94.05 | C
ON-ORBIT WET | 139340.00 | 26421.33 | 
Adapter | 10570.17 | 2044.81 | C
Launch Mass | 149910.17 | 29573.15 | C

## Slide 151: Orbiter Mass Statement (1/2) - SC
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
Payload | 377.00 | 77.43 | C
Structure | 260.00 | 500.00 | C
Thermal Control | 1378.00 | 1015.00 | C
Power | 195.00 | 304.81 | C
TT&C | 91.00 | 8.39 | C
On-Board Processing | 52.00 | 3.91 | C
ADC | 78.00 | 5.10 | C
Propulsion | 130.00 | 0.00 | C
Other (balance + launch) | 39.00 | 10.00 | C
TPS | 0.00 | 367.23 | C
Budget Total | 2600.00 | 1924.64 | 
Margin | 910.00 | 1585.36 | 

## Slide 152: Orbiter Mass Statement (2/2) - SC
Spacecraft Mass Statement |  |  | 
Subsystem | Budget (kg) | Current (kg) | Status
On-Orbit Dry | 2600.00 | 1924.64 | 
*Propellant | 1430.00 | 0.00 | C
*Pressurant | 6.40 | 0.00 | C
ON-ORBIT WET | 4030.00 | 1924.64 | 
Adapter | 354.27 | 195.31 | C
Launch Mass | 4384.27 | 2487.18 | C
* No need to propulsion system with the S/C will be carried by Venus’ winds

## Slide 153: Total System Power Statement
Spacecraft Power Statement |  |  | 
Subsystem | Budget (W) | Current (W) | Status
Thermal Control | 157.42 | 14.14 | C
Attitude Control | 112.44 | 328.43 | C
Power | 56.22 | 328.98 | C
C&DS | 95.58 | 182.00 | C
COMMs | 129.31 | 418.40 | C
Propulsion | 5.62 | 2.42 | C
Mechanism | 5.62 | 4.50 | C
Total | 562.22 | 1278.87 | 
Margin | 506.00 | -210.65 | 
Payload | 170.00 | 125.50 | C
ON ORBIT POWER | 732.22 | 1404.37 | 

## Slide 154: Launch Vehicle: SLS
Space Launch System:
  *Cost: < 4.1 Billion
  Source: NASA
  Fairing diameter: 8.4 meters
  Payload capacity: 37,900 kg
  Max : 130
* Launch cost isn’t part of budget as mentioned by AIAA RFP

## Slide 155: Cost Estimation Models
Models utilized
  UCSM8 Non-recurring Cost Estimating Relationship
  UCSM8 Spacecraft Recurring Cost Estimating Relationship
  NASA Instrument Cost Model (NICM) Non-recurring Cost Model
  Small Satellite Cost Model (SSCM)
Assumptions
  Utilized CPI (Consumer price index) to account for inflation

## Slide 156: Cost Estimation Model Analysis
Cost Estimation Model (All) |  |  | 
Cost Model | *Total Cost (2010) | *Total Cost (2023) | *Total Cost (2035)
USCM8 (Recurring) + NICM | 180 | 254 | 323
USCM8 (Non-recurring) + NICM | 553 | 780 | 991
SSCM + NICM | 8597 | 12135 | 15402
* Cost in million of dollars

## Slide 157: USCM8 Cost Model Analysis (1/2)
USCM8 (Non-recurring) |  |  | 
WBS Element | *Total Cost (2010) | *Total Cost (2023) | *Total Cost (2035)
SC Bus | 272.29 | 384.34 | 487.77
Structure and Thermal Control | 96.75 | 136.56 | 173.31
ADCS | 1.65 | 2.33 | 2.96
Electrical Power System | 19.60 | 27.67 | 35.11
Propulsion | 0.004 | 0.01 | 0.01
Telemetry | 26.92 | 37.99 | 48.22
Communications Payload | 47.85 | 67.54 | 85.72
Integration, Assembly, and Test | 62.43 | 88.12 | 111.83
* Cost in million of dollars

## Slide 158: USCM8 Cost Model Analysis (2/2)
USCM8 (Non-recurring) |  |  | 
WBS Element | *Total Cost (2010) | *Total Cost (2023) | *Total Cost (2035)
Program Level | 136.58 | 192.78 | 244.66
Aerospace Ground Equipment | 36.73 | 51.85 | 65.81
Total | 700.80 | 989.18 | 1255.39
* Cost in million of dollars

## Slide 159: NICM Non-Recurring Cost Model Analysis
NICM (Non-recurring) |  |  | 
WBS Element | *Total Cost (2010) | *Total Cost (2023) | *Total Cost (2035)
Optics Planetary | 13.10 | 18.49 | 23.46
Management | 1.26 | 1.78 | 2.26
Systems Engineering | 5.58 | 7.88 | 10.00
Product Assurance | 1.08 | 1.53 | 2.73
Integration and Test | 2.04 | 2.88 | 3.66
Total | 23.06 | 32.55 | 42.11
* Cost in million of dollars

## Slide 160: Cost Statement
Total Cost Table |  |  | 
WBS Element | *Total Cost (2010) | *Total Cost (2023) | *Total Cost (2035)
USCM8 (Non-recurring) | 700.80 | 192.78 | 244.66
NICM | 23.06 | 32.55 | 42.11
Software | 2.39 | 3.37 | 4.27
Total | 726 | 1025 | 1302
* Cost in million of dollars

## Slide 161: Similar Vehicles Comparison
Vehicles Comparsion |  |  |  | 
Vehicle | *Total Cost (2010) | *Total Cost (2023) | *Total Cost (2035) | Source
MERV | 726 | 1025 | 1302 | 
Magellan (1989) | 952.81 | 2325.64 | 2951.50 | NASA
Venus Express (2005) | 262.00 | 443.14 | 562.40 | ESA
Lucy (2022) | 989.1 | 1396.13 | 1771.85 | GAO
* Cost in million of dollars

## Slide 162: Conclusion
Cost Analysis
  *Expected Cost: 780 million (2023) | 991 million (2035)
  Utilized USCM8 (non-recurring) and NICM cost models
  Accounted for inflation using CPI relations
  Within 1 billion budget outlined by the AIAA RFP
Spacecraft Budgets
  Total spacecraft mass: 29573.15 kg (25.11 % over budget)
    Within SLS’s payload mass capacity of 37,900 kg
  Total spacecraft power: 1404.37W (47.86% over budget)
* Removing cost of program and grounds station construction
Notes: Design A
  Total time = 302.74 days
  Total DV = 17.74 km/s
Design B
  Total time = 292.14 days
  Total DV = 13.3141 km/s

## Slide 163: Reference Slide
[1] Brown, C. D. (2002). Elements of spacecraft design. American Institute of Aeronautics and Astronautics, Inc.
[2] Edberg, D. (2022). Spacecraft Design, Development, & Operation.
[3] Europa Clipper Instrument Summaries. (n.d.-a). https://europa.nasa.gov/internal_resources/379/ScienceInstruments_031422_Public.pdf
[4] Instructions for competitors obtaining own launch RevB - NASA. (n.d.-b). https://www.nasa.gov/wp-content/uploads/2023/02/instructions-for-competitors-obtaining-own-launch-revb.pdf
[5] NASA. (n.d.-a). Artemis. NASA. https://www.nasa.gov/specials/artemis/
[6] NASA. (2023, February 16). Maspex. NASA. https://europa.nasa.gov/spacecraft/instruments/maspex/
[7] NASA. (n.d.-b). NASA Technical Reports Server (NTRS). NASA. https://ntrs.nasa.gov/
[8] NASA. (n.d.-b). Radar Imager for mars’ subsurface exploration (RIMFAX). NASA. https://mars.nasa.gov/mars2020/spacecraft/instruments/rimfax/

## Slide 164: Reference Slide
[9] Space mission engineering: The new smad. (2011). . Amazon Publishing.
[10] Wikimedia Foundation. (2023, October 5). Xenon. Wikipedia. https://en.wikipedia.org/wiki/Xenon
[11] Wikimedia Foundation. (2023a, October 1). Psyche (spacecraft). Wikipedia. https://en.wikipedia.org/wiki/Psyche_(spacecraft)

## Slide 165
Thank you!